## Slide 1
PROPOSAL FOR LRDE · BENGALURU · RESTRICTED
Altera
AI Compute Platform for LRDE
Sovereign training hardware and Altera Agilex™ FPGA inference for radar signal intelligence, AESA processing aids, and real-time classification.
Audience: LRDE leadership & radar AI teams · Focus: Radar / AESA / EW-adjacent AI · Version 1.0 · Aug 2026

## Slide 2
AGENDA
What we will cover
A complete path from LRDE training data to fielded FPGA inference inside radar timelines.
1. LRDE mission fit & AI opportunities
2. End-to-end architecture
3. Training hardware (secure GPU lab)
4. Inference on Altera Agilex FPGAs
5. Software toolchain & MLOps
6. LRDE use-case packages
7. Security & sovereignty
8. PoC roadmap & next steps

## Slide 3
LRDE CONTEXT
Radar AI where it matters
LRDE designs ground-based, shipborne, airborne, and space-related radar systems — AI must respect real-time DSP pipelines and SWaP.
AESA & multifunction
Fire-control, surveillance, 4D radars.
Multi-mode interleaved operation needs deterministic assistive AI.
Signal intelligence
Pulse / emitter classification.
LPI detection aids, clutter/anomaly separation on I/Q & spectrograms.
Advanced research
Hypersonic cues, stealth-detection aids, FOPEN features.
Netted-radar fusion — train secure, infer at the sensor.

## Slide 4
PROBLEM
Gaps in today’s radar AI path
Training
• Classified I/Q & track data cannot leave LRDE
• Cloud GPUs unsuitable for air-gapped labs
• Weak experiment / model lineage
Inference
• GPUs struggle with radar SWaP & latency budgets
• Need tight coupling to JESD / ADC / beam data
• Long program life vs short GPU cycles
Required outcome
A sovereign stack that lets LRDE:
• Train on-prem on radar datasets
• Compile models to FPGA AI IP
• Deploy inside ERP / processor cabinets or payloads
• Update bitstreams without board respins

## Slide 5
ARCHITECTURE
Train once · Infer on Agilex
LRDE SECURE LAB Radar Data Vault → GPU Training Cluster → Model Registry │ ONNX / OpenVINO IR ▼ Quantize + Accuracy Gates → FPGA AI Suite (dla_compiler) ┌──────────────┼──────────────┐ Hostless Agilex SoC Agilex 5 PCIe Agilex 7 (ERP / payload) (edge node) (shelter / C2)
GPU
Secure training
OpenVINO
IR + hetero runtime
Agilex
Field inference

## Slide 6
TRAINING HARDWARE
Air-gapped radar AI training lab
Sized for LRDE model development on spectrograms, RD maps, tracks, and multi-sensor fusion sets.
Component | Reference spec | Role for LRDE
GPU nodes | 8× datacenter GPUs/node, dual CPU, 1–2 TB RAM | CNN / transformer training
Fabric | NVLink + InfiniBand NDR / RoCE | Distributed training
Storage | Encrypted 0.5–2 PB object / parallel FS | I/Q archives, checkpoints
CPU ETL | High-core labeling & feature nodes | RD maps, CFAR labels, sim data
Security | Air gap, bastion MFA, optional diode | Sovereign model export only

## Slide 7
TRAINING SOFTWARE
ML stack inside the wire
Frameworks & ops
• PyTorch / TensorFlow (air-gapped registry)
• DeepSpeed / FSDP for large models
• Slurm or Kubernetes + Apptainer
• MLflow / DVC for lineage
Radar-specific data path
• I/Q → STFT / RD / spectrogram pipelines
• Synthetic + trial data blending
• Golden sets for accuracy gates
• Signed ONNX / IR promotion
Handoff to inference
Export ONNX → OpenVINO IR → FPGA AI Suite compile → signed bitstream / network-bin for LRDE platforms.

## Slide 8
INFERENCE HARDWARE
Altera Agilex™ for radar timelines
FPGAs sit next to the exciter–receiver–processor chain — reconfigurable AI without breaking determinism.
Device | INT8 class* | LRDE placement
Agilex 3 | ~2.6 TOPS | Miniaturized / SoC radar sensors
Agilex 5 E-Series | ~26 TOPS | Compact processors, mobile radars
Agilex 5 D-Series | ~152 TOPS | Multi-channel classification
Agilex 7 I/M-Series | ~89 TOPS class | ERP co-process, PCIe, shelters
*Architecture- and IP-dependent; sized per model with FPGA AI Suite Architecture Optimizer.

## Slide 9
DEPLOYMENT
Form factors for LRDE systems
Hostless / DDR-free
AI IP in fabric beside DSP.
Lowest latency for pulse/window classifiers inside ERP.
SoC (HPS)
On-chip Linux + AI IP.
Ideal for transportable radars and edge fusion nodes.
PCIe / OFS card
Look-aside acceleration in operation shelters and lab validation racks.
JESD204 / ADC attach · Aurora / Ethernet sensor nets · Bitstream encryption · Long defence lifecycle

## Slide 10
WHY ALTERA
FPGA vs GPU for LRDE inference
Criterion | GPU | Altera FPGA
Latency determinism | Batch / driver variable | Pipeline-friendly, stable
RF / DSP coupling | Needs host staging | Direct fabric I/O
Power in cabinet / payload | High | Lower W for fixed nets
Model update | Driver + app stack | Bitstream / network-bin
Program longevity | Short SKU cycles | 10–15+ year class support

## Slide 11
SOFTWARE TOOLCHAIN
From PyTorch to radar bitstream
Train (PyTorch) → ONNX → OpenVINO convert_model / ovc → IR (.xml/.bin) → Quantize (INT8 / FP16) + golden accuracy gate → FPGA AI Suite dla_compiler --march <arch.arch> → Architecture Optimizer (area ↔ FPS) → Bit-accurate OpenVINO emulation → Quartus Prime integrate AI IP → bitstream → Runtime: FPGA or HETERO:FPGA,CPU (or hostless)
Core tools: OpenVINO · FPGA AI Suite · Quartus Prime · optional Open FPGA Stack (OFS).

## Slide 12
LRDE PACKAGES
Three PoC-ready use cases
1. Emitter / pulse ID
Spectrogram CNN on Agilex 7 hostless or PCIe.
Continuous windows, deterministic latency for EW-adjacent radar modes.
2. Target / clutter assist
RD-map or tracklet classifier on Agilex 5.
Aids discrimination for fighters, slow movers, false-alarm reduction.
3. Netted fusion node
Multi-radar feature fusion on Agilex 7 PCIe in shelter C2.
Signed model hot-swap after trials.

## Slide 13
SECURITY
Sovereignty by design
Data residency
I/Q, tracks, and labels never leave LRDE premises.
Air gap
Training isolated; controlled diode export of IR/bitstreams only.
Bitstream trust
Encryption, authentication, anti-tamper options on Agilex.
Indian partners
Board / SOM qualification with SI & DPSU ecosystem.

## Slide 14
ROADMAP
Phased engagement with LRDE
0
Discovery — 4–6 weeks
Workload survey (2 models), latency/SWaP envelopes, success metrics with ERP owners.
1
PoC — 8–12 weeks
Port models to Agilex eval kits; accuracy vs golden set; latency report for radar windows.
2
Pilot — 3–6 months
Rugged module or PCIe in processor cabinet; training-cluster slice; MLOps baseline.
3
Scale — program-driven
Production SOM/PCIe, environmental qualification, ILS & field update process.

## Slide 15
REFERENCE BOM
What LRDE would procure
Training lab
• GPU nodes + IB fabric
• Encrypted storage
• Hardened MLOps stack
Inference & tools
• Agilex 7 PCIe + Agilex 5 kits
• Quartus Prime + FPGA AI Suite
• OpenVINO + enablement services
Detailed commercial annex after discovery workshop. See BOM_Reference.md.

## Slide 16
CALL TO ACTION
Recommended next steps
1. Workshop
2-day architecture session at LRDE — nominate radar AI & ERP stakeholders.
2. Select models
Pick two flagship networks (e.g. pulse ID + RD classifier) for Phase-1 PoC.
3. Lock gates
Agree accuracy, window latency, and power budgets before compile.
4. SOW
Issue technical SOW + commercial annex for PoC kits and FAE support.
Prepared for LRDE, DRDO Bengaluru · Inference: Altera Agilex + FPGA AI Suite