## Slide 1
ALTERA | SPACE / NTN PAYLOAD
RX / TX Direct Radiating Array Architecture
AGRW027/039 device clusters | Direct-RF 64 Gsps | Separate TX/RX silicon paths (9 devices)
RX Uplink 14.0-14.5 GHz | 32 beams
TX Downlink 10.7-12.75 GHz | 40/32 beams
RX DRA — UPLINK
14.0–14.5 GHz · 32 spot beams · 4× AGRW027/039 (ADC side)
Antenna /
Feed Array
LNA
Front-End
RX DEVICE CLUSTER
Device 1
8 ADC · Beams 1–8
Device 2
8 ADC · Beams 9–16
Device 3
8 ADC · Beams 17–24
Device 4
8 ADC · Beams 25–32
PER DEVICE DSP PIPELINE
Direct-RF ADC
64 Gsps · 1st Nyquist
DDC
Digital Beamforming
4-color · 8-way spatial reuse
UL Channelizer
4 × 125 MHz / beam
DVB-RCS2 / 3GPP-NTN
Low-PHY handoff
Quad-core Arm Cortex-A53 (HPS) per device · Multi-device phase-sync IP for coherent beamforming
Conservative isolation option: TX and RX on physically separate silicon / RF paths
Onboard Router / Switch Fabric
58 Gbps SerDes interconnect between device clusters and Feeder-link stage
TX DRA — DOWNLINK
10.7–12.75 GHz · 40 spot beams (NTN) / 32 (DVB-S2X) · 5× AGRW027/039 (DAC side)
PER DEVICE DSP PIPELINE
DVB-S2X / 3GPP-NTN
Low-PHY framer
Digital Beamforming
4-color · 8–10 way spatial reuse
DUC
Direct-RF DAC
64 Gsps synthesis
TX DEVICE CLUSTER
Device 1
8 DAC · Beams 1–8
Device 2
8 DAC · Beams 9–16
Device 3
8 DAC · Beams 17–24
Device 4
8 DAC · Beams 25–32
Device 5 *
8 DAC · Beams 33–40
HPA
Front-End
Antenna /
Feed Array
* Device 5 carries 4 spare/idle DAC channels when operating in DVB-S2X-only mode (32 beams)
Total: 9 devices (5 TX + 4 RX) · Cleanest TX→RX isolation · Phase-sync across cluster
Altera Confidential
AGRW027/039 · Ku-band DRA Payload Architecture
Altera Confidential
3