## Slide 1
ALTERA | SPACE / NTN PAYLOAD
Onboard Router / Switch Fabric
Regenerative digital cross-connect between RX cluster, TX cluster, and Feeder-link stage
RX Device Cluster
4× AGRW027/039 · Beams 1–32 Post DVB-RCS2 / NTN Low-PHY
TX Device Cluster
5× AGRW027/039 · Beams 1–40 Pre DVB-S2X / NTN Low-PHY
Onboard Router / Switch Fabric
58 Gbps-class SerDes trunks · Packet / TB switching (not raw ADC/DAC samples)
Feeder-link Stage
Gateway modem · TT&C overlay · Ground trunk
Direct-RF sample paths stay inside each device. The fabric only moves demodulated user-plane,
control-plane, and feeder traffic — preserving separate TX/RX silicon for RF isolation.
Altera Confidential
Onboard Router / Switch Fabric
1

## Slide 2
ONBOARD FABRIC — DETAIL
Ports, SerDes class, and traffic engineering
Port groups
RX ports — 4 devices (Beams 1–32)
TX ports — 5 devices (Beams 1–40)
Feeder ports — gateway / TT&C
Control — HPS / management
Logical Clos / crossbar preferred
58 Gbps-class SerDes
Lane class (PAM4), not aggregate
Altera F-tile / equivalent
2–4 lanes per RX/TX device
4–8 lanes to feeder trunk
1+1 / N+1 spare for FDIR
What crosses the fabric
Post-Low-PHY packets / TBs
NOT 64 Gsps ADC/DAC IQ
Beam maps & ACM control
Sync / timing messages
Telemetry & health
Traffic classes
Class | Direction | Content | Priority
User plane | RX→TX / RX↔Feeder / Feeder→TX | Demodulated packets / transport blocks | High, shaped
Control plane | Bidirectional | Beam maps, ACM, NTN signaling | Highest
Sync / timing | Fabric-wide | Schedules, timing packets | Reserved
Telemetry | Devices → Feeder / HPS | BER, thermal, HPS logs | Best effort
Multicast | Fabric → TX set | Broadcast / group beams | Configurable
Altera Confidential
Onboard Router / Switch Fabric
2

## Slide 3
ONBOARD FABRIC — FUNCTIONS
Switching functions and control plane
UL→DL cross-connect
Regenerative beam-to-beam
forwarding after Low-PHY
Mesh across color reuse
Feeder gateway
Concentrate user traffic
to/from ground modem
Often fattest trunk
Beam remap
Update forwarding tables
on steer / recolor
Aligns with DBFN maps
FDIR / spare
Steer around failed device
Use TX Device 5 spare
in DVB-S2X-only mode
Replication
1:N broadcast / NTN
SIB-like content
Ephemeris floods
RF isolation keep
TX/RX silicon stay split
Only digital meets here
Cleanest TX→RX isolation
Control plane: each device HPS (Arm Cortex-A53) owns local config; fabric controller owns route/beam tables,
SerDes health, and FDIR. Same logical fabric ports apply to Option A (AGRW SoC) and Option B (Agilex 7 + AFE7950).
Altera Confidential
Onboard Router / Switch Fabric
3

## Slide 4
ONBOARD FABRIC — SIZING
Example SerDes lane plan (Direct-RF SoC option)
Illustrative starting point — close after traffic engineering (modulation, coding, duty cycle, overbooking).
Link | Suggested lanes | Approx capacity class | Notes
Each RX device ↔ fabric | 2–4 × 58G | ~100–200 Gbps raw | Post-Low-PHY UL + control
Each TX device ↔ fabric | 2–4 × 58G | ~100–200 Gbps raw | DL framer input + replication
Fabric ↔ feeder stage | 4–8 × 58G | ~200–400 Gbps raw | Gateway aggregate + protect
Control / debug | 1–2 × lower-rate | Mgmt Ethernet / PCIe | Out-of-band OK
Aggregate (order) | — | Multi-100G fabric | Efficiency < line rate
Bandwidth reminder
Fabric carries post-demod bits, not 64 Gsps samples
Size for peak ACM + ~20–40% overhead
Feeder trunk often dominates
Option B (Agilex 7 + TI)
Same logical ports: 4 RX + 5 TX + feeder
SerDes from each Agilex 7 into fabric
JESD204C stays local FPGA↔AFE7950
Altera Confidential
Onboard Router / Switch Fabric
4